## Slide 1: *Customer* – Heat Pump use case Performance and price indication
HP ONLY steam generation
Max. Output
REMARK: all numbers and information on this page are preliminary, indicative and non-binding
*standard heat pump installation based on terminal points and scope description on following pages
**standard 5-years service agreement, further described on following pages
  Heat input: 10.0 MWth Cooling from 65 ˚C → 35 ˚C Mass flow ~ 78.0 kg/s
Heat source characteristics
  Heat output: 15.0 MWth Water 90 °C → 120 °C steam Mass flow ~ 6 kg/s
Heat sink characteristics
Heat pump characteristics
  COP: 2.59 (Gross) Required electric power: ~ 5.8 MWel (incl. HP auxiliaries) Refrigerant: R1233ZD(E)
  Estimated CAPEX: xxx Mio € (standard heat pump installation*)
  Estimated service cost: ~ xxx k€/a** (± 30% accuracy, std. service)
  Estimated footprint: approx.
  Estimated project duration: ~20 – 24 months
Solution price & characteristics
35 °C, Water
Heat Pump
90 °C, Water
120 °C, Water
65 °C, Water